## Slide 1
CONCLUSIONS & FUTURE WORK
DESIGN CONCEPTS
METHODOLOGY
BACKGROUND
OBJECTIVE
DESIGN CRITERIA
COMPONENT TESTING
Road Curvature Decomposition for Autonomous Guidance
Ricardo Jacome, Mechanical Engineering Graduate Research Assistant, University of Nebraska -Lincoln
ACKNOWLEDGMENTS: MwRSF’s Outdoor Proving Grounds Manager, Test Technicians, and Students for conducting tests
Develop a method for discretizing geospatial data and providing vehicle path guidance for autonomous vehicles.
Vehicle autonomy has been touted as the future of transportation, but there are significant challenges which remain to be addressed.
Tremendous growth has been achieved in “Advanced Driver Assistance Systems”
Need low-cost, crashworthy solution functional for many impact conditions and with narrow footprint
Example: bridge adjacent to intersection
Objectives & Criteria
Impact conditions determined by length of need
4 dynamic bogie tests were conducted on the Dragnet Vehicle Arresting Barrier
Jacome, Sweigard, Stolle
Review existing systems and applications
Develop narrow-footprint concepts
Component test & measure reactions
Fifteen concepts generated, and ranked based on analysis of: 1) safety performance 2) maintenance and repair costs 3) effort to develop concept 4) installation cost
Highest-ranked concepts: 1) net attenuator/end terminal 2) sand barrels/end terminal 3) bullnose with secondary energy absorber
Bogie Test Matrix
Initial Configuration
Second Configuration
Net attenuator selected for testing and stopped a 5,259-lb bogie vehicle traveling at roughly 60 mph in 43 ft or less
Component testing suggested design would work under variety of impact conditions, speeds, and angles, and was versatile for installation
Design must be paired with other crashworthy crash cushion (in development) – future work
Energy Absorber Failure
IRA-4: 5,259-lb bogie at 59.5 mph and 90 degree impact angle on center
IRA-3: 5,259-lb bogie at 58.0 mph and 60 degree impact angle off center
Occupant Risk Summary