## Slide 1: MATC Smart Barrier – Path Generation
Ricardo Jacome
Midwest Roadside Safety Facility
University of Nebraska-Lincoln
Pool Fund Sample Presentation
4/15/2019

## Slide 2: Autonomous Vehicle Evolution
To Drive Autonomously:
Based on SAE Recommended Practice J3016 from 2018.
Dynamic Driving Tasks (DDT)
Steering/Avoidance
Braking/Accelerating
Automated Driving Systems (ADS)
Levels 0,1,2 – Driver Performs DDT’s
Level 3,4,5 – ADS Performs DDT’s
From 2000 and 2018, Level 4 has been reached.

## Slide 3: Limitations: Sensors
On GPS
From Federal Aviation Administration:
On May 11, 2016, the reported global average User Range Error was ≤0.715 m (2.3 ft.), 95% of the time.
This Error is Enough to have a Vehicle off the Road
On Object Detection
Tencent Keen Security Lab
On March, 2019, Tesla’s Autopilot was tested for Lane Detection accuracy, and mistook stickers for lane marks.
Conclusions: Level 5 is not yet a reality
Notes: https://www.gps.gov/systems/gps/performance/accuracy/
https://electrek.co/2019/04/01/tesla-autopilot-hacker-tricked/

## Slide 4: What’s Missing?
Current Vehicle Technology is Focused on using Current Infrastructure made for humans
Current Infrastructure is not made for autonomous vehicles
Infrastructure can evolve to adapt to new Vehicles

## Slide 5: MATC SMART Barrier
Project of 3 Main Parts Consisting of
Updates on Infrastructure for:
Local Trilateration
Local Path Generation
Modular Vehicle Navigation

## Slide 6: Local Trilateration
Vehicle to Infrastructure (V2I) Communications
RSU Roadside Units
  Local GPS Location
OBU On-Board Unit
  Vehicle Information Transfer
Objective: Find Vehicle Position in Local Frame
Notes: Sanguesa, J. Sensing Traffic Density Combining V2V and V2I
Wireless Communications

## Slide 7: Local Path Generation
Once Establishing a Local Position:
Use Off-line Data
  To reduce computation cost on OBU
Local Path Generation
  Send in the Form of Steering Wheel Angle
Objective: To Generate a Path with the Smallest Storage Cost Possible

## Slide 8: Modular Vehicle Navigation
Adjust Path for Individual Vehicles
  Vehicle guidance is dependent on vehicle parameters
  Unique Paths need to be generated per vehicle data

## Slide 9: Taxonomy of Levels

## Slide 10: Normal-Tangential Accel.
  Where:
    = Second Derivative Magnitude of the Path ‘s’
    = Instantaneous Radius of Curvature
    v = Velocity of the Vehicle
    = Unit Vector Tangent to Path
    = Unit Vector Normal to Path
Vehicle Centerline

## Slide 11: Road Sampling Example

## Slide 12: Road Slicing

## Slide 13: Multiple Sections of Slices

## Slide 14: Ackerman Steering
At low speeds, this geometric relationship holds true:
For Ackerman Steering, it is assumed that the value is an average of both wheels together.
Notes: Images from Fundamentals of Vehicle Dynamics – Thomas D. Gillespie

## Slide 15: Modified Ackerman Steering
A bicycle model takes both front and rear wheels into a single front and rear wheel.
At High Speeds, the wheels develop lateral forces that create slippage.
This is denoted by the Slip Angle which is used in the Modified Ackerman Steering Formula:
Notes: Images from Fundamentals of Vehicle Dynamics – Thomas D. Gillespie

## Slide 16: Steering Gradient Factors
  Where:
    L = Wheelbase
    = Radius of Curvature
    K = Understeer Gradient (Dependent on many Factors)
    = Centripetal Acceleration
Notes: L = Wheelbase of Vehicle
V = The velocity of the vehicle
Rho = Instantaneous Radius of Curvature
Wf = Distributed Front Weight of Vehicle
Wr = Distributed Rear Weight of Vehicle
Caf = Cornering Stiffness of the Front Tires
Car = Cornering Stiffness of the Rear Tires
G = Gravitational Acceleration Constant

## Slide 17: Steering Gradient Behavior

## Slide 18: Hidden Slide