## Slide 1: MATC Smart Barrier Project
Ricardo Jacome
Michael Sweigard
Midwest Roadside Safety Facility
University of Nebraska-Lincoln
03/14/19

## Slide 2: Outline
Project Background and Objective
Phase One
  ABS Friction Testing
Phase Two (current work)
  Goals
  Path generation
  Path following
Future Work

## Slide 3: Project Background
53% fatal crashes related to road departures between 2014-2016 - FHWA
  Drift-off road, overcorrection, failure to negotiate, avoidance maneuver
Notes: Figure 1 Examples of ROR Crashes (images take from NHTSA’s NASS CDS)
Roll overs
Roadside fixed objects 1/3
Return to lane

## Slide 4: Project Background
Current advanced driver-assistance systems (ADAS) have considerable limitations

## Slide 5: Project Goals
Develop a vehicle-to-roadside infrastructure (V2I) system to prevent roadside departures
Five phases
Literature Review
System Modeling
Model Verification/ Validation
Finalize System
Prototyping and Hardware
Year One
Year Two
Year Three
Year Four
Year Five

## Slide 6: Literature Review Topics
Current Vehicle Market
Data Filters
Vehicle Control
Traffic Management
Cybersecurity

## Slide 7: Abs testing & critical stability analysis

## Slide 8: ABS Background
Notes: Junhui, L., and Jianqiang, Road Surface Condition Detection based on Road Surface Temperature and Solar Radiation, Volume 6, 2010 International Conference on Computer, Mechatronics, Control and Electronic Engineering, , IEEE, New York, New York, August 2010, pages 4-7.

## Slide 9: ABS Friction Testing
Evaluate effectiveness of ABS on split-mu friction roads
  Evaluated performance limits
  Define emergency braking threshold
Develop vehicle braking model to estimate behavior for different surfaces
  Simplified linear model
  Average frictional values
Notes: 1) We need to determine when the vehicle must take action and/or warn the driver when a vehicle's path toward the roadside is critical.
2) A critical factor in vehicle safety and stability is the ability to brake.
3) The longer we can wait to apply brakes and start steering, without compromising safety, the less "false positive" corrections will be issued and drivers will be more likely to use system
4) A possible safety risk involves a vehicle partly on the paved road and partly on another surface
5) We conducted split-mu testing & baseline (benchmark) tests to evaluate what those effects are
6) Using those test results, we generated curves of effective, average friction & ramp-up times for different surfaces per wheel
7) Results were used to generate approximation models for computer simulation purposes

## Slide 10: Braking Model
Develop vehicle braking model to estimate behavior for different surfaces
  Simplified linear model
  Average frictional values
Notes: 1) We need to determine when the vehicle must take action and/or warn the driver when a vehicle's path toward the roadside is critical.
2) A critical factor in vehicle safety and stability is the ability to brake.
3) The longer we can wait to apply brakes and start steering, without compromising safety, the less "false positive" corrections will be issued and drivers will be more likely to use system
4) A possible safety risk involves a vehicle partly on the paved road and partly on another surface
5) We conducted split-mu testing & baseline (benchmark) tests to evaluate what those effects are
6) Using those test results, we generated curves of effective, average friction & ramp-up times for different surfaces per wheel
7) Results were used to generate approximation models for computer simulation purposes

## Slide 11: ABS Friction Testing

## Slide 12: ABS Friction Testing
Notes: ABSF-5 sand to grass

## Slide 13: ABS Friction Results
 | ABSF-1 (concrete) | ABSF-2 (concrete) | ABSF-3 (gravel) | ABSF-3 (grass) | ABSF-4 (gravel) | ABSF-4 (grass) | ABSF-5 (sand) | ABSF-5 (grass) | ABSF-6 (sand) | ABSF-6 (grass)
Total Braking Time (sec) | 3.0 | 3.2 | 5.4 |  | 5.6 |  | 5.7 |  | 5.2 | 
Total Braking Distance (ft) | 127 | 147 | 227 |  | 214 |  | 206 |  | 230 | 

## Slide 14: ABS Friction Results
ABSF-7 (split-mu concrete/ gravel) | ABSF-7 (split-mu concrete/ grass) | ABSF-8 (split-mu concrete/ gravel) | ABSF-8 (split-mu concrete/ grass) | ABSF-9 (split-mu concrete/ sand) | ABSF-9 (split-mu concrete/ grass) | ABSF-10 (split-mu concrete/ sand) | ABSF-10 (split-mu concrete/ grass)
4.4 |  | 4.1 |  | 4.9 |  | 4.3 | 
197 |  | 173 |  | 221 |  | 197 | 

## Slide 15: ABS Friction Results
Chart: 
| Concrete | Gravel to Grass | Sand to Grass | Split-mu gravel to grass | split-mu sand to grass
Stopping Time | 3.0625 | 5.4775 | 5.4525 | 4.248 | 4.613
Chart: 
| Concrete | Gravel to Grass | Sand to Grass | Split-mu gravel to grass | split-mu sand to grass
Stopping Distance | 136.5187 | 220.3206 | 218.0086 | 185.1444 | 209.2613

## Slide 16
 | Ramp Up Slope (g's/s) | Ramp Up time | Max/Min Coefficient of Friction | Average Coefficient of Friction | Transition Time (sec)
ABSF-4 (gravel) | 1.61 | 0.31 | 0.81/0.34 | 0.57 | N/A
ABSF-4 (grass) | N/A | N/A | 0.52/0.31 | 0.40 | 0.43
Notes: Explain Breaking Event
Multiple methods for determining slope: Fixed ends and weighted average
Average value for friction surface
Transition based on integrated stopping distance

## Slide 17: Development of Desired Path Generation Techniques

## Slide 18: Phase II: Path Generation
Motivation
  For vehicle to remain on road, need critical parameters
    Vehicle location with respect to road (lane) edges
    Road path vector
    Vehicle velocity vector
    Orientation (heading) angle
  Current methods of AV requires vehicles to determine location & guidance autonomously

## Slide 19: Phase II: Path Generation
GPS Application for Guidance
  Conventional GPS accuracy: +/- 7 to 10 ft
  Update frequency: 10 Hz
  Increased precision requires network of connected base stations, extensive data
  Not available in all locations (e.g., mountains)
New Approach
  Rethink guidance on local + global scale using long-range fixed roadside reference network

## Slide 20: Background: Vehicle Dynamics
Forces on Straight Line Motion
Forces on Curvilinear Motion

## Slide 21: Normal-Tangential Accelerations
  Where:
    = Second Derivative Magnitude of the Path ‘s’
    = Instantaneous Radius of Curvature
    v = Velocity of the Vehicle
    = Unit Vector Tangent to Path
    = Unit Vector Normal to Path
Vehicle Centerline

## Slide 22: Road Slicing Background
Velocity Vector is assumed close to Heading Angle of Vehicle
Centripetal Acceleration
  By definition at an instantaneous point.
  We can relate to
Y
X
X
Y

## Slide 23: Road Slicing Technique
Slice the Road in small sections and find a curvature of each slice
  Scanning the road with sensors such as lidar
  Aerial/satellite map & custom plots
Find velocity vector perpendicular to road slice
Generate map of velocity vector, magnitude based on physical position

## Slide 24: Road Sampling Example

## Slide 25: Road Slicing

## Slide 26: Multiple Sections of Slices

## Slide 27: Velocity Vector Angle
Approach is limited to Directions Only as of now
Research is being done on how to relate Ackerman Steering Angle and Road Slicing Technique

## Slide 28: Ackerman Steering
At low speeds, this geometric relationship holds true:
For Ackerman Steering, it is assumed that the value is an average of both wheels together.
Notes: Images from Fundamentals of Vehicle Dynamics – Thomas D. Gillespie

## Slide 29: Modified Ackerman Steering
A bicycle model takes both front and rear wheels into a single front and rear wheel.
At High Speeds, the wheels develop lateral forces that create slippage.
This is denoted by the Slip Angle which is used in the Modified Ackerman Steering Formula:
Notes: Images from Fundamentals of Vehicle Dynamics – Thomas D. Gillespie

## Slide 30: Steering Gradient Factors
  Where:
    L = Wheelbase
    = Radius of Curvature
    K = Understeer Gradient (Dependent on many Factors)
    = Centripetal Acceleration
    W’s = Distributed Weight of the Vehicle
    C’s = Cornering Stiffness
Notes: L = Wheelbase of Vehicle
V = The velocity of the vehicle
Rho = Instantaneous Radius of Curvature
Wf = Distributed Front Weight of Vehicle
Wr = Distributed Rear Weight of Vehicle
Caf = Cornering Stiffness of the Front Tires
Car = Cornering Stiffness of the Rear Tires
G = Gravitational Acceleration Constant

## Slide 31: Steering Gradient Behavior

## Slide 32: Hidden Slide

## Slide 33: Develop Model of Road Paths

## Slide 34: Trajectory Control
Goal:
  Use vehicle velocity vector angle to safety traverse the roadway
Simplified vehicle model
PID Control

## Slide 35: PID Control

## Slide 36: PID Control
Notes: Kp works to get to the desired value as fast as possible but can overshoot due to momentum
Kd applies correction if error is small but slope is big, dampens system, reduces overshoot
Ki eliminates stead state error

## Slide 37: PID Control
Notes: Kd applies correction if error is small but slope is big, dampens system, reduces overshoot

## Slide 38: PID Control
Notes: Ki eliminates stead state error

## Slide 39: Model Base Equations
Notes: Time step of 0.1 seconds

## Slide 40: Path Following Model

## Slide 41: Model Performance

## Slide 42: Model Performance

## Slide 43: Model Performance

## Slide 44: Model Performance

## Slide 45: Model Performance

## Slide 46: Road Generation
From AASHTO Design Guide
  R – Radius (ft)
  V - Velocity (ft/s)
  e - superelevation (%)
  f – side friction factor
  L- Length of transition (ft)
  V – Velocity (ft/s)
  R – curve radius (ft)
  C – change lateral acceleration
Notes: Chose values that would minimize the radius for a more dynamic path

## Slide 47: Path Following Model

## Slide 48: Model Performance

## Slide 49: Model Performance

## Slide 50: Model Performance

## Slide 51: Model Performance

## Slide 52: Model Performance

## Slide 53: Future Work
Path Generation
  Path generation optimization
  Develop relationships for road curvature
  Obtain heading angles
Path Following
  Minimization of data points
  PID optimization
  Correction for error accumulation
  Add in advanced vehicle model
Triangulation method
Notes: Understeer gradient, maximum friction level